## Slide 1
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
1
Gas-phase polyolefin transitions create off-grade at scale
GLOBAL ADDRESSABLE PRODUCTION
≈194
Mt / year
PE ≈112 · PP ≈82
45% OF GLOBAL PLASTICS
ILLUSTRATIVE OFF-GRADE
≈554
t / transition
11.5 h · 48.2 t/h average
ILLUSTRATIVE GAS-PHASE TRANSITION
INFERRED
LAB SAMPLE
SOURCE
ON SPEC
OFF-GRADE
NEW GRADE
ON SPEC
DENSITY
kg/m³
918 → 921
MFR
g/10 min
2 → 20
917.5–918.5
DESTINATION TARGET 920.5–921.5
1.6–2.4
DESTINATION TARGET 18–22
-2
0
3
6
9
12
HOURS FROM GRADE CHANGE
DENSITY READY 2.9 h
✓
LICENSED FOOTPRINT
200
UNIPOL PE REACTOR LINES
>110
UNIPOL PP REACTOR LINES
>130
SPHERIPOL LICENSED LINES
Notes: Lead with off-grade volume and market scale. Simulated transition TR-05 remained off grade for 11.5 hours. Average simulated production rate during the off-grade window was 48.2 tonnes per hour. The simulated transition therefore produced approximately 554 tonnes of off-grade resin. PlasticsEurope reported 430.9 Mt of global plastics production in 2024. PE accounted for 26.0%. PP accounted for 19.0%. A 26.0% PE share implies approximately 112 Mt of PE. A 19.0% PP share implies approximately 82 Mt of PP. Combined PE and PP production reached approximately 194 Mt. Univation reported 200 licensed UNIPOL PE reactor lines. Grace reported more than 110 all-gas-phase UNIPOL PP reactor lines. LyondellBasell reported more than 130 Spheripol lines. The density and MFR traces show one mechanism that prolonged off-grade production. ModularSimulator commit da3ec63 generated the property traces. Transition TR-05 moved density from 918 to 921 kilograms per cubic metre. Transition TR-05 moved MFR from 2 to 20 grams per ten minutes. Density entered the 920.5 to 921.5 destination range at 2.87 hours. MFR entered the 18 to 22 destination range at 11.50 hours. Both properties then remained in range for 30 minutes. MFR extended the transition window by 8.63 hours after density settled. Gray markers show simulated hourly lab samples. Lab error used a 0.28 kilogram-per-cubic-metre density standard deviation. MFR lab error used a 6% relative standard deviation. Target bands stepped at hour zero. Red target bands marked the off-grade period. Green target bands marked the source and destination on-spec periods. [Sources] - PlasticsEurope, Plastics the Fast Facts 2025 (2024 preliminary data): https://plasticseurope.org/wp-content/uploads/2025/09/PE_TheFacts_25_digital-1pager-scrollable.pdf - Univation, 200 licensed UNIPOL PE reactor lines and >65 Mt/year design capacity: https://www.univation.com/en-us/news-and-events/univation-celebrates-achieving-200-licensed-reactor-lines-milest.html - Grace, >110 all-gas-phase UNIPOL PP reactor lines and close to 300 grades: https://grace.com/newsroom/press-releases/2023-press-releases/grace-expands-presence-china-pc-guangxi-signing-second-unipol-pp-technology-license/ - LyondellBasell, >130 Spheripol licensed lines and >35 Mt licensed capacity: https://www.lyondellbasell.com/globalassets/lyb/our-solutions/technologies/petrochemical/polypropylene/cta/2025_jul_tec_spheripol_techflyer_rebrand.pdf - Illustrative off-grade calculation from repository simulation output: 48.2 t/h average production rate × 11.5 h off-grade duration = approximately 554 t/transition. - Repository source: /home/alden/projects/seeq-demo/.plans/00-master-plan.md - Simulator source: ModularSimulator commit da3ec63 through the isolated archive at /home/alden/projects/seeq-demo/.cache/modular-simulator-da3ec63-stage1 - Simulation output: /home/alden/projects/seeq-demo/.cache/presentation-simulation/output/transition_metadata.json (TR-05 duration 11.5 h) - Simulation output: /home/alden/projects/seeq-demo/.cache/presentation-simulation/output/transitions.csv (TR-05 property traces and hourly lab samples) [/Sources]

## Slide 2
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
2
Shorter transitions recover saleable resin
RECOVERED RESIN
Chart: TRANSITIONS / YEAR
| 12 | 24 | 36
Recovered resin | 375 | 750 | 1125
Estimated recovery | 37.5 | 75 | 112.5
RECOVERED RESIN (t/year)
EST. RECOVERY
24 / YEAR · 30 MIN
750 t / year
$75k / year*
* 500 KTA · 8,000 h/year · 30 min reduction · $0.10/kg margin · commodity PE ≈$1/kg.
BENEFITS BEYOND RECOVERED RESIN
REDUCED
TRIMMING
IMPROVED
SCHEDULING
EFFICIENCY
BETTER
CONSTRAINT
MANAGEMENT
CONTINUOUS TRANSITION INTELLIGENCE
1
FIND PEERS
2
ALIGN EVENTS
3
ISOLATE DRIVERS
4
RECOMMEND CHANGE
↻ REPEAT AS PROCESS DRIFTS
compare transitions → isolate drivers → update recipe → repeat
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Present an illustrative sensitivity model. A 500 KTA plant operating 8,000 hours per year produces 62.5 tonnes per hour. A 30-minute reduction recovered 31.25 tonnes per transition. Twelve transitions recovered 375 tonnes per year. Twenty-four transitions recovered 750 tonnes per year. Thirty-six transitions recovered 1,125 tonnes per year. The line shows annual recovered-resin volume. The left axis shows tonnes per year. The right axis shows estimated margin recovery in thousands of dollars per year. The margin assumption is $0.10 per kilogram of on-grade resin over off-grade resin. The margin assumption equals $100 per tonne. Estimated margin recovery reached $75,000 per year for the 24-transition case. Commodity polyethylene is shown at roughly $1 per kilogram for scale. S&P Global assessed US LLDPE at $849 per metric tonne in August 2025. That assessment equals $0.85 per kilogram. Optimized transitions can reduce trimming needs. More predictable transition durations can improve production scheduling. Better visibility into limiting conditions can improve constraint management. Transition Intelligence finds comparable transitions. Transition Intelligence aligns events. Transition Intelligence isolates drivers. Transition Intelligence recommends a recipe or SOP change. A team repeats the workflow as process conditions drift. An engineer decides whether to use each recommendation. [Sources] - Illustrative sensitivity model calculated for this deck. Assumptions: 500 KTA plant, 8,000 operating hours/year, 12/24/36 events/year, 30-minute transition-time reduction, and $0.10/kg on-grade resin margin over off-grade resin. Derived values: 500,000 ÷ 8,000 = 62.5 t/h; 62.5 × 0.5 = 31.25 recovered tonnes/event; 12 × 31.25 = 375 recovered tonnes/year; 24 × 31.25 = 750 recovered tonnes/year; 36 × 31.25 = 1,125 recovered tonnes/year; $0.10/kg = $100/tonne; estimated recovery = recovered tonnes × $100/tonne. - S&P Global Commodity Insights, Spot polyethylene prices sink amid oversupply, weak demand across Americas, August 21, 2025. US LLDPE butene assessment: $849/mt FAS Houston, equivalent to $0.849/kg: https://www.spglobal.com/energy/en/news-research/latest-news/chemicals/082125-spot-polyethylene-prices-sink-amid-oversupply-weak-demand-across-americas - Repository source: /home/alden/projects/seeq-demo/.plans/00-master-plan.md - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 3
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 1 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 4
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 2 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 5
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 3 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 6
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 4 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 7
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
C₂ PP
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 5 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 8
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
C₂ PP
CATALYST FEED
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 6 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 9
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
C₂ PP
CATALYST FEED
PRESSURE
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 7 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 10
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
C₂ PP
CATALYST FEED
PRESSURE
SAME TRANSITION · DIFFERENT DATES
JAN 10
9.0 h
JAN 14
8.2 h
JAN 17
9.1 h
8.2–9.1 h
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 8 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 11
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
3
Coupled dynamics make transition analysis difficult
NORMALIZED ACROSS EACH SIGNAL'S OBSERVED RANGE
0%
50%
100%
0
2
4
6
8
10
HOURS FROM GRADE CHANGE
MFR
DENSITY
H₂/C₂
C₄/C₂
C₂ PP
CATALYST FEED
PRESSURE
SAME TRANSITION · DIFFERENT DATES
JAN 10
9.0 h
JAN 14
8.2 h
JAN 17
9.1 h
8.2–9.1 h
•
Coupled signals leave multiple plausible explanations.
•
Closed-loop feedback correlates inputs with disturbances, complicating system identification.
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Click-through build frame 9 of 9. Start with MFR. Add density. Add H2-to-C2 ratio. Add C4-to-C2 ratio. Add ethylene partial pressure. Add catalyst feed rate. Add total reactor pressure on a full-width plot. The following frame introduces the three-transition duration comparison. That comparison frame also adds all seven normalized traces from TR-02 and TR-04. The comparison and conclusion frames therefore show 21 traces. Solid lines show TR-06. Dashed lines show TR-02. Dotted lines show TR-04. Hold the comparison frame before advancing. The following frame states the conclusion. Temperature is excluded because the simulator did not generate temperature. Each signal is normalized from zero to 100 percent across its observed range within each simulated transition. Normalization makes different engineering units comparable without implying equal economic sensitivity. Coupled signals leave multiple plausible explanations. Closed-loop feedback correlates plant inputs with disturbances. A model fit that ignores the feedback-induced correlation can be biased. Three simulated transitions used the same 1630-to-2210 grade direction. Duration ranged from 8.2 to 9.1 hours across January 10, January 14, and January 17. [Sources] - Repository simulation output: /home/alden/projects/seeq-demo/data/transitions.csv (TR-02, TR-04, and TR-06 MFR, density, hydrogen mole ratio, comonomer mole ratio, ethylene partial pressure, catalyst feed, and total pressure) - Repository simulation output: /home/alden/projects/seeq-demo/data/transition_metadata.json (TR-02, TR-04, and TR-06 durations and dates) - Forssell and Ljung, Closed-loop identification revisited, Automatica 35(7), 1999, DOI 10.1016/S0005-1098(99)00022-9: https://www.sciencedirect.com/science/article/pii/S0005109899000229/pdf - Mejari, Piga, and Bemporad, A bias-correction method for closed-loop identification of Linear Parameter-Varying systems, Automatica 87, 2018, DOI 10.1016/j.automatica.2017.09.014: https://www.sciencedirect.com/science/article/abs/pii/S0005109817304843 - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]

## Slide 12
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
4
Contextualized advisory agent for transition optimization
SITE EVIDENCE
SEEQ PLATFORM
AGENTIC INVESTIGATION
ENGINEERING DECISION
PROCESS DATA
trends · labs · events
CONTROL STATE
modes · saturation · bias
PROCESS KNOWLEDGE
constraints · implications · SOPs
TRANSITION HISTORY
peers · prior actions · outcomes
APC
targets · constraints · tuning
SEEQ INTELLIGENCE
CONTEXTUALIZED DATA
signals · assets · conditions
ANALYTICS + ML
events · models · calculations
KNOWLEDGE
documents · prior analyses
AGENT TOOLS
search · trend · calculate
AUGMENTS EXISTING ANALYTICS + ML
TRANSITION AGENT
1
LOOK UP
↓
2
COMPARE
↓
3
CHECK HISTORY
↓
4
EXPLAIN
evidence · drivers · impact
INTERACTIVE Q&A
faster learning · fewer knowledge gaps
RECIPE / SOP CHANGE
APC TUNING CHANGE
OPERATING LIMIT CHANGE
APPROVE · REVISE · DEFER
SITE CONFIGURATION
tags · grades · constraints · documents · APC
REUSABLE CORE
workflow · tools · reasoning steps · evaluation
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Suggested timing: two and a half minutes. Site evidence includes process trends, laboratory samples, events, controller modes, actuator saturation, controller bias, operating constraints, SOPs, transition history, prior actions, and APC configuration. Seeq contextualizes time-series data and events. Seeq stores calculations, prior analyses, and documents. Existing analytics and machine-learning models remain available to the workflow. The agent augments those methods with contextual lookup, tool use, and interactive reasoning. A transition agent looks up relevant context. The agent compares peer events. The agent checks candidate explanations against historical peer transitions, process constraints, and source documents. The workflow does not assume a digital twin. The agent explains evidence, drivers, estimated impact, and tradeoffs. Interactive Q&A lets users probe the evidence. The interaction supports faster learning. The interaction can reduce knowledge gaps across users, shifts, and sites. An engineer can approve, revise, or defer a recipe, SOP, APC tuning, or operating-limit change. Site-specific configuration maps tags, grades, constraints, documents, and APC structures. A reusable core preserves agent workflow, tool contracts, reasoning steps, and evaluation across customers. [Sources] - Seeq, Introducing Seeq Intelligence, March 3, 2026: https://www.seeq.com/resources/press-releases/introducing-seeq-intelligence/ - Seeq Knowledge Base, Agent Q: https://support.seeq.com/latest/cloud/agent-q - Seeq Knowledge Base, Agent Builder: https://support.seeq.com/latest/cloud/seeq-agent-builder - Seeq Knowledge Base, Analyze Data: https://support.seeq.com/latest/cloud/analyze-data - Seeq Workbench product page: https://www.seeq.com/product/workbench/ - Repository source: /home/alden/projects/seeq-demo/.plans/03-agent-tools.md [/Sources]

## Slide 13
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
5
A reusable core enables an eight-week first-site launch
ESTIMATED IMPLEMENTATION
W1
W2
W3
W4
W5
W6
W7
W8
ALIGN
grade pair
success metric
CONTEXTUALIZE
signals · events
limits · states
CONFIGURE
tools · knowledge
agent workflow
VALIDATE
backtest · SME review
safeguards
LAUNCH
train users
track value
REUSABLE CORE
agent workflow · tools · UI · evaluation
moves to the next unit
SITE CONFIGURATION
signals · grades · constraints · APC
validated with site engineers
8 WEEKS FIRST SITE · 2–4 WEEKS SUBSEQUENTLY
Estimate assumes data and integration availability.
TRANSITION INTELLIGENCE
GAS-PHASE POLYOLEFIN TRANSITION DECISION SUPPORT
Notes: Suggested timing: one and a half minutes. A first-site estimate spans eight weeks. Week one aligns a priority grade pair and a measurable success criterion. Weeks two and three contextualize signals, events, operating limits, and control states. Weeks four and five configure agent tools, knowledge, and workflow. Weeks six and seven backtest historical transitions. Site subject-matter experts review evidence and safeguards. Week eight launches a governed workflow. Training and value tracking begin at launch. A reusable core carries agent workflow, tools, UI, and evaluation to another unit. Site configuration maps signals, grades, constraints, documents, and APC. A next-unit estimate spans two to four weeks when data and integrations are available. Timeline values are planning assumptions for an initial sales discussion. [Sources] - Implementation estimate calculated for this deck. Assumptions: data and integrations are available, one priority grade pair defines initial scope, site SMEs can review weekly, and recommendations remain advisory. Estimated first site: 8 weeks. Estimated next unit: 2–4 weeks. - Seeq Knowledge Base, Agent Builder supports reusable multi-step custom agents: https://support.seeq.com/latest/cloud/seeq-agent-builder - Seeq, Introducing Seeq Intelligence: https://www.seeq.com/resources/press-releases/introducing-seeq-intelligence/ - Repository source: /home/alden/projects/seeq-demo/.plans/00-master-plan.md - Repository source: /home/alden/projects/seeq-demo/.plans/04-demo-integration.md [/Sources]